## Slide 1: The Processor
Prepared by Dr. Andrew Jung

## Slide 2: Introduction
CPU performance factors
  Instruction count
    Determined by ISA and compiler
  CPI and Cycle time
    Determined by CPU hardware
We will examine two MIPS implementations
  A simplified version
  A more realistic pipelined version
Simple subset, shows most aspects
  Memory reference: lw, sw
  Arithmetic/logical: add, sub, and, or, slt
  Control transfer: beq, j

## Slide 3: Instruction Execution
PC  instruction memory, fetch instruction
Register numbers  register file, read registers
Depending on instruction class
  Use ALU to calculate
    Arithmetic result
    Memory address for load/store
    Branch target address
  Access data memory for load/store
  PC  target address or PC + 4

## Slide 4: CPU Overview

## Slide 5: Multiplexers
Can’t just join wires together
  Use multiplexers

## Slide 6: Control

## Slide 7: Logic Design Basics
Information encoded in binary
  Low voltage = 0, High voltage = 1
  One wire per bit
  Multi-bit data encoded on multi-wire buses
Combinational element
  Operate on data
  Output is a function of input
State (sequential) elements
  Store information

## Slide 8: Combinational Logic
A logic system whose blocks do not contain memory and hence compute the same output given the same input.
Truth table
  describe any combinational logic function.
  It grows in size quickly and may not be easy to understand.

## Slide 9: Truth Table
Inputs |  |  | Outputs |  | 
A | B | C | D | E | F
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 1 | 0 | 1
  Three inputs A, B, C, and three outputs D, E, and F.
  D is true if at least one input is true.
  E is true if exactly two inputs are true.
  F is true only if all three inputs are true.

## Slide 10: Boolean Algebra
OR operator: +
And operator: ∙
NOT operator: Ᾱ
Express the logic function with logic equation.
Identity Law: A + 0 = A and A ∙ 1 = A
Zero and One laws: A + 1 = 1 and A ∙ 0 = 0
Inverse Law: A + Ᾱ = 1 and A ∙ Ᾱ = 0
Commutative law: A + B = B + A and A ∙ B = B ∙ A
Associative law: A + (B + C) = (A + B) + C and A ∙ (B ∙ C) = (A ∙ B) ∙ C
Distributive Law: A ∙ (B + C) = (A ∙ B) + (A ∙ C) and A + (B ∙ C) = (A + B) ∙ (A +C)
DeMorgan’s Theoreum:

## Slide 11: Logic Equation
D = A + B + C
E = ((A ∙ B) + (A ∙ C) + (B ∙ C)) ∙
F = A ∙ B ∙ C

## Slide 12: Gates
Standard drawing for an AND gate, OR gate, and an inverter, shown from left to right. The signals to the left of each symbol are the inputs, while the output appears on the right. The AND and OR gates both have two inputs. Inverters have a single input.

## Slide 13: Gates
Logic gate implementation of using explicit inverts on the left and bubbled inputs and outputs on the right. This logic function can be simplified to

## Slide 14: Combinational Logic
Decoders
  A logic block that has an n-bit input and 2n outputs, where only one output is asserted for each input combination.

## Slide 15: Multiplexors
Selector
Three parts
  A decoder that generates n signals, each indicating a different input value.
  An array of n AND gates, each combining one of the inputs with a signal from decoder.
  A single large OR gate that incorporates the outputs of the AND gates.

## Slide 16: Multiplexors
A two-input multiplexor on the left and its implementation with gates on the right. The multiplexor has two data inputs (A and B), which are labeled 0 and 1, and one selector input (S), as well as an output C. Implementing multiplexors in Verilog requires a little more work, especially when they are wider than two inputs.

## Slide 17: Sum of products
A form of logical representation that employs a logical sum(OR) of products(terms joined using the AND operator)

## Slide 18: Sum of products
Show the sum of products representation for the following truth table for D.
Inputs |  | Outputs | 
A | B | C | D
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 19: Sum of products
There are four product terms, since the function is true(1) for four different input combination.
Thus, we can write the function for D as the sum of these:

## Slide 20: Activity
On Blackboard…