## Slide 1: Memory Access
Prepared by Dr. Andrew Jung

## Slide 2: Registers
Registers have both numeric and symbolic names
$0 $zero - special register for constant zero
$1 $at - assembler temporary
$2 - $3 $v0 - $v1 - values for function returns and expression evaluation
$4 - $7 $a0 - $a3 - arguments for functions
$8 - $15 $t0 - $t7 - temporary registers
$16 - $23 $s0 - $s7 - saved registers
$24 - $25 $t8 - $t9 - more temporary registers
$26 - $27 $k0 - $k1 - reserved for OS kernel
$28 $gp - global pointer
$29 $sp - stack pointer
$30 $fp - frame pointer
$31 $ra - return address

## Slide 3: Hexadecimal Numbers
Recall that memory is addressed in binary (32 or 64-bit)
If we use base 16 or hexadecimal numbers, these values can be represented in a more compact manner.
1000 -> 8
1001 -> 9
1010 -> A (10 decimal)
1011 -> B (11 decimal)
1100 -> C (12 decimal)
1101 -> D (13 decimal)
1110 -> E (14 decimal)
1111 -> F (15 decimal)
0000 -> 0
0001 -> 1
0010 -> 2
0011 -> 3
0100 -> 4
0101 -> 5
0110 -> 6
0111 -> 7

## Slide 4: Data Storage In Arrays
Recall that one of the reasons we need to look at binary and hex values is so we can understand how data is stored in memory.
In particular we will look at arrays.
Arrays are stored contiguously in memory. This means each data element is placed one right after the other.

## Slide 5: An Analysis of Arrays
In C and Java, we generally index into arrays without regard for the size of a data element.
For example, given the following Java or C style arrays:
int [] iArr = new int[10] or int iArr[10];
char [] cArr = new char[10]; or char cArr[10];
we access cArr[2] or iArr[5] in the same manner regardless of how the data is stored.
We can do the same with objects.

## Slide 6: Arrays
We access cArr[2] or iArr[5] in the same manner regardless of how the data is stored. We can do the same with objects.
cArr[2] means give me the data at memory address cArr + 2
iArr[5] means give me the data at memory address iArr + 5*4, assuming a 32-bit system
Assume the array name is a label that refers to an offset in memory.
Assuming memory is an array, we are saying memory[label + array index].
cArr[2] means give me the data at memory address cArr + 2
iArr[5] means give me the data at memory address iArr + 5*4, assuming 32-bit integers.

## Slide 7: An Example in C
Given the following example:
int arr[10];
for(i = 0; i < 10; i++) {
arr[i] = 1+i;
printf("arr[%d] is %d\n",
i,arr[i]);
}

## Slide 8: A Similar Example in C
int arr[10];
for(i = 0; i < 10; i++) {
*(arr+i) = 1+i;
printf("arr[%d] is %d\n",
i,*(arr+i));
}

## Slide 9: Converting to Assembly – Declaring a statically allocated array
Declaration and initialization to zero of an integer array is performed in the .data section of an assembly program
Syntax:
  Label: .word 0:arraySize
Example:
  intArr: .word 0:10

## Slide 10: Converting to Assembly
Assume the array name is a label that refers to an offset in memory.
Assuming memory is an array, we are saying Memory[label + array index].
Let's assume for now the label is stored in a register like $s1
We tell the assembler we are referring to data in a memory address as follows:
0($s1)

## Slide 11: Array Offsets in Assembly
We tell the assembler we want to access an offset into memory by changing the value in front of $s1
offset($s1) - Note: offset is a 16 bit signed integer
Example: 4($s1) - 4 bytes past the memory address stored in $s1
8($s1) - 8 bytes past the memory address stored in $s1
Data at a memory address must be loaded before it may be used.

## Slide 12: Loading Array Data
When using 32-bit data units (words), the lw or load word instruction is used to load data from memory into a register.
Syntax:
lw destination_register, source_address
Example
lw $s2, 0($s1) #load the data at memory
#address $s1 into $s2
lw $s2, 4($s1) #load the data at memory
#address $s1 + 4 into $s2

## Slide 13: Issues with Low Level Memory
Warning: Memory is stored differently on different processors!
Memory has an endianness, referring to the order in which the bits in memory are stored for each byte/word.
Big endian - first byte in a word is the most significant bits, last byte is the least significant bits.
Little endian - first byte in a word is the least significant bits, last byte is the most significant bits.
MIPS is a Big Endian Machine.

## Slide 14: Load Word
lw is a "move" command.
It moves data out of memory and into registers.
Notice that integer/32-bit arrays are indexed by segments of four bytes.
We can easily move through such an array.
Assume the address of our array is in $s1 and we wish to get to index 5
  li $t1, 5 # load 5 into $t1
  add $t1, $t1, $t1 # now $t1 is 10 (it's doubled)
  add $t1, $t1, $t1 # now $t1 is 20 (it's doubled # again)
  add $t1, $s1, $t1 # now $t1 contains the address of # index 5 of our array
  lw $t2, 0($t1) #load the value at array[5] into $t2

## Slide 15: Store Word
Another "move" command is sw.
sw moves data out of a register into memory.
sw = store word
Syntax:
sw data_source, destination_address

## Slide 16: Store Word
We can store a value at a position in the integer array myIntegerArray.
li $t3, 432
sw $t3, 8($t1)
Here we store the value 432 in place of the value 3 in location 2 of the myIntegerArray.