## Slide 1: Computer Abstractions and Technology
Chapter 1

## Slide 2: The Computer Revolution
Progress in computer technology
  Underpinned by Moore’s Law
Makes novel applications feasible
  Computers in automobiles
  Cell phones
  Human genome project
  World Wide Web
  Search Engines
Computers are pervasive

## Slide 3: Classes of Computers
Desktop computers
  Designed to deliver good performance to a single user at low cost usually executing 3rd party software, usually incorporating a graphics display, a keyboard, and a mouse
Servers
  Used to run larger programs for multiple, simultaneous users typically accessed only via a network and that places a greater emphasis on dependability and (often) security
Supercomputers
  A high performance, high cost class of servers with hundreds to thousands of processors, terabytes of memory and petabytes of storage that are used for high-end scientific and engineering applications
Embedded computers (processors)
  A computer inside another device used for running one predetermined application

## Slide 4: Review: Some Basic Definitions
Kilobyte – 210 or 1,024 bytes
Megabyte– 220 or 1,048,576 bytes
  sometimes “rounded” to 106 or 1,000,000 bytes
Gigabyte – 230 or 1,073,741,824 bytes
  sometimes rounded to 109 or 1,000,000,000 bytes
Terabyte – 240 or 1,099,511,627,776 bytes
  sometimes rounded to 1012 or 1,000,000,000,000 bytes
Petabyte – 250 or 1024 terabytes
  sometimes rounded to 1015 or 1,000,000,000,000,000 bytes
Exabyte – 260 or 1024 petabytes
  Sometimes rounded to 1018 or 1,000,000,000,000,000,000 bytes

## Slide 5: The PostPC Era

## Slide 6: The PostPC Era
Personal Mobile Device (PMD)
  Battery operated
  Connects to the Internet
  Hundreds of dollars
  Smart phones, tablets, electronic glasses
Cloud computing
  Warehouse Scale Computers (WSC)
  Software as a Service (SaaS)
  Portion of software run on a PMD and a portion run in the Cloud
  Amazon and Google

## Slide 7: What You Will Learn
How programs are translated into the machine language
  And how the hardware executes them
The hardware/software interface
What determines program performance
  And how it can be improved
How hardware designers improve performance
What is parallel processing

## Slide 8: Understanding Performance
Algorithm
  Determines number of operations executed
Programming language, compiler, architecture
  Determine number of machine instructions executed per operation
Processor and memory system
  Determine how fast instructions are executed
I/O system (including OS)
  Determines how fast I/O operations are executed

## Slide 9: Below the Program
System software
  Operating system – supervising program that interfaces the user’s program with the hardware (e.g., Linux, MacOS, Windows)
    Handles basic input and output operations
    Allocates storage and memory
    Provides for protected sharing among multiple applications
  Compiler – translate programs written in a high-level language (e.g., C, Java) into instructions that the hardware can execute
Systems software
Applications software
Hardware

## Slide 10: Below the Program, Con’t
High-level language program (in C)
  swap (int v[], int k)
  (int temp;
  temp = v[k];
  v[k] = v[k+1];
  v[k+1] = temp;
  )
Assembly language program (for MIPS)
  swap: sll $2, $5, 2
  add $2, $4, $2
  lw $15, 0($2)
  lw $16, 4($2)
  sw $16, 0($2)
  sw $15, 4($2)
  jr $31
Machine (object, binary) code (for MIPS)
  000000 00000 00101 0001000010000000
  000000 00100 00010 0001000000100000
    . . .
C compiler
assembler
Notes: Computer only understands zeros and ones – instructions of 0’s and 1’s
Early programmers found representing machine instructions in a symbolic notation – assembly language
And developed programs that translate from assembler to machine code
Eventually, programmers found working even in assembler too tedious so migrated to higher-level languages and developed compilers that would translate from the higher-level languages to assembler

## Slide 11: Advantages of Higher-Level Languages ?
Higher-level languages
As a result, very little programming is done today at the assembler level
  Allow the programmer to think in a more natural language and for their intended use (Fortran for scientific computation, Cobol for business programming, Lisp for symbol manipulation, Java for web programming, …)
  Improve programmer productivity – more understandable code that is easier to debug and validate
  Improve program maintainability
  Allow programs to be independent of the computer on which they are developed (compilers and assemblers can translate high-level language programs to the binary instructions of any machine)
  Emergence of optimizing compilers that produce very efficient assembly code optimized for the target machine
Notes: For lecture

## Slide 12: Under the Covers
Five classic components of a computer – input, output, memory, datapath, and control
datapath + control = processor (CPU)

## Slide 13: Touchscreen
Post-PC device
Supersedes keyboard and mouse
Resistive and Capacitive types
  Most tablets, smart phones use capacitive
  Capacitive allows multiple touches simultaneously

## Slide 14: Opening the Box
Capacitive multitouch LCD screen
3.8 V, 25 Watt-hour battery
Computer board

## Slide 15: Inside the Processor
Apple A5

## Slide 16: Inside the Processor (CPU)
Datapath: performs arithmetic operations on data
Control: sequences datapath, memory, and I/O devices according to the instructions of the program
Cache memory
  Small fast SRAM memory for immediate access to data

## Slide 17: Instruction Set Architecture (ISA)
Idea to improve design is abstraction.
ISA, or simply architecture – the abstract interface between the hardware and the lowest level software that encompasses all the information necessary to write a machine language program, including instructions, registers, memory access, I/O, …
  Enables implementations of varying cost and performance to run identical software
The combination of the basic instruction set (the ISA) and the operating system interface is called the application binary interface (ABI)
  ABI – The user portion of the instruction set plus the operating system interfaces used by application programmers. Defines a standard for binary portability across computers.

## Slide 18: A Safe Place for Data
Volatile main memory
  Loses instructions and data when power off
Non-volatile secondary memory
  Magnetic disk
  Flash memory
  Optical disk (CDROM, DVD)

## Slide 19: Networks
Communication, resource sharing, nonlocal access
Local area network (LAN): Ethernet
Wide area network (WAN): the Internet
Wireless network: WiFi, Bluetooth

## Slide 20: Technology Trends
Electronics technology continues to evolve
  Increased capacity and performance
  Reduced cost
Year | Technology | Relative performance/cost | 
1951 | Vacuum tube | 1 | 
1965 | Transistor | 35 | 
1975 | Integrated circuit (IC) | 900 | 
1995 | Very large scale IC (VLSI) | 2,400,000 | 
2013 | Ultra large scale IC | 250,000,000,000 | 
DRAM capacity
§1.5 Technologies for Building Processors and Memory

## Slide 21: Moore’s Law
Courtesy, Intel ®
Dual Core Itanium with 1.7B transistors
feature size
&
die size
In 1965, Intel’s Gordon Moore predicted that the number of transistors that can be integrated on single chip would double about every two years
Log Scale

## Slide 22: Technology Scaling Road Map (ITRS)
Year | 2004 | 2006 | 2008 | 2010 | 2012
Feature size (nm) | 90 | 65 | 45 | 32 | 22
Intg. Capacity (BT) | 2 | 4 | 6 | 16 | 32
Fun facts about 45nm transistors
  30 million can fit on the head of a pin
  You could fit more than 2,000 across the width of a human hair
  If car prices had fallen at the same rate as the price of a single transistor has since 1968, a new car today would cost about 1 cent
Notes: International Technology Roadmap for Semiconductors