## Slide 1: Performance Metrics
Prepared by Dr. Andrew Jung

## Slide 2: Defining Performance
Which airplane has the best performance?

## Slide 3: Throughput versus Response Time
Response time (execution time) – the time between the start and the completion of a task
  Important to individual users
Throughput (bandwidth) – the total amount of work done in a given time
  Important to data center managers
Will need different performance metrics as well as a different set of applications to benchmark embedded and desktop computers, which are more focused on response time, versus servers, which are more focused on throughput

## Slide 4: Defining (Speed) Performance
To maximize performance, need to minimize execution time
performanceX = 1 / execution_timeX
  If X is n times faster than Y, then
performanceX execution_timeY
-------------------- = --------------------- = n
performanceY execution_timeX
Decreasing response time almost always improves throughput
Notes: Increasing performance requires decreasing execution time

## Slide 5: Relative Performance Example
If computer A runs a program in 10 seconds and computer B runs the same program in 15 seconds, how much faster is A than B?
We know that A is n times faster than B if
performanceA execution_timeB
-------------------- = --------------------- = n
performanceB execution_timeA
15
------ = 1.5
10
The performance ratio is
So A is 1.5 times faster than B

## Slide 6: Performance Factors
CPU execution time (CPU time) – time the CPU spends working on a task
  Does not include time waiting for I/O or running other programs
CPU execution time # CPU clock cycles
for a program for a program
= x clock cycle time
CPU execution time # CPU clock cycles for a program
for a program clock rate
= -------------------------------------------
Can improve performance by reducing either the length of the clock cycle or the number of clock cycles required for a program
or
Notes: Many techniques that decrease the number of clock cycles also increase the clock cycle time

## Slide 7: Review: Machine Clock Rate
Clock rate (clock cycles per second in MHz or GHz) is inverse of clock cycle time (clock period)
CC = 1 / CR
one clock period
10 nsec clock cycle => 100 MHz clock rate
5 nsec clock cycle => 200 MHz clock rate
2 nsec clock cycle => 500 MHz clock rate
1 nsec (10-9) clock cycle => 1 GHz (109) clock rate
500 psec clock cycle => 2 GHz clock rate
250 psec clock cycle => 4 GHz clock rate
200 psec clock cycle => 5 GHz clock rate
Clock period: duration of a clock cycle
  e.g., 250ps = 0.25ns = 250×10–12s
Clock frequency (rate): cycles per second
  e.g., 4.0GHz = 4000MHz = 4.0×109Hz
Notes: A clock cycle is the basic unit of time to execute one operation/pipeline stage/etc.

## Slide 8: Improving Performance Example
A program runs on computer A with a 2 GHz clock in 10 seconds. What clock rate must computer B run at to run this program in 6 seconds? Unfortunately, to accomplish this, computer B will require 1.2 times as many clock cycles as computer A to run the program.
CPU timeA CPU clock cyclesA
clock rateA
= -------------------------------
CPU clock cyclesA = 10 sec x 2 x 109 cycles/sec = 20 x 109 cycles
CPU timeB 1.2 x 20 x 109 cycles
clock rateB
= -------------------------------
clock rateB 1.2 x 20 x 109 cycles
6 seconds
= ------------------------------- = 4 GHz
Notes: For lecture

## Slide 9: Clock Cycles per Instruction
Not all instructions take the same amount of time to execute
  One way to think about execution time is that it equals the number of instructions executed multiplied by the average time per instruction
Clock cycles per instruction (CPI) – the average number of clock cycles each instruction takes to execute
  A way to compare two different implementations of the same ISA
# CPU clock cycles # Instructions Average clock cycles
for a program for a program per instruction(CPI)
= x
CPU Time = # Instructions X CPI X Clock Cycle Time
= # Instructions X CPI
---------------------------
Clock Rate

## Slide 10: CPI Example
Computer A: Cycle Time = 250ps, CPI = 2.0
Computer B: Cycle Time = 500ps, CPI = 1.2
Same ISA
Which is faster, and by how much?
A is faster…
…by this much

## Slide 11: CPI in More Detail
If different instruction classes take different numbers of cycles
Weighted average CPI
Relative frequency
  Where Istruction Counti is the count (percentage) of the number of instructions of class i executed
  CPIi is the (average) number of clock cycles per instruction for that instruction class
  n is the number of instruction classes

## Slide 12: CPI Example
Alternative compiled code sequences using instructions in classes A, B, C
Class | A | B | C
CPI for class | 1 | 2 | 3
IC in sequence 1 | 2 | 1 | 2
IC in sequence 2 | 4 | 1 | 1
Sequence 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Sequence 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5

## Slide 13: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc

## Slide 14: Exercises