## Slide 1: Instructions-Computer Language I
Prepared by dr. Andrew Jung

## Slide 2: Instruction Set
The repertoire of instructions of a computer
The vocabulary of commands understood by a given architecture
Different computers have different instruction sets
  But with many aspects in common
Early computers had very simple instruction sets
  Simplified implementation
Many modern computers also have simple instruction sets

## Slide 3: The MIPS Instruction Set
Used as the example throughout the book
Stanford MIPS commercialized by MIPS Technologies (www.mips.com)
Large share of embedded core market
  Applications in consumer electronics, network/storage equipment, cameras, printers, …
Typical of many modern ISAs
  See MIPS Reference Data tear-out card, and Appendixes B and E

## Slide 4: Arithmetic Operations
Add and subtract, three operands
  Two sources and one destination
add a, b, c # a gets b + c
All arithmetic operations have this form
Design Principle 1: Simplicity favors regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost

## Slide 5: Arithmetic Operations
a = b + c + d + e
  add a, b, c //The sum of b and c is placed in a
  add a, a, d //The sum of b, c, and d is now in a
  add a, a, e //The sum of b, c, d, and e is now in a

## Slide 6: Arithmetic Operations
a = b + c;
d = a – e;
  add a, b, c
  sub d, a, e

## Slide 7: Arithmetic Example
C code:
f = (g + h) - (i + j);
Compiled MIPS code:
add t0, g, h # temp t0 = g + h add t1, i, j # temp t1 = i + j sub f, t0, t1 # f = t0 - t1

## Slide 8: Register Operands
Arithmetic instructions use register operands
MIPS has a 32 × 32-bit register file
  Use for frequently accessed data
  Numbered 0 to 31
  32-bit data called a “word”
Assembler names
  $t0, $t1, …, $t9 for temporary values
  $s0, $s1, …, $s7 for saved variables
Design Principle 2: Smaller is faster
  c.f. main memory: millions of locations

## Slide 9: Register Operand Example
C code:
f = (g + h) - (i + j);
  f, …, j in $s0, …, $s4
Compiled MIPS code:
add $t0, $s1, $s2 add $t1, $s3, $s4 sub $s0, $t0, $t1

## Slide 10: Registers
Registers have both numeric and symbolic names
$0 $zero - special register for constant zero
$1 $at - assembler temporary
$2 - $3 $v0 - $v1 - values for function returns and expression evaluation
$4 - $7 $a0 - $a3 - arguments for functions
$8 - $15 $t0 - $t7 - temporary registers
$16 - $23 $s0 - $s7 - saved registers
$24 - $25 $t8 - $t9 - more temporary registers
$26 - $27 $k0 - $k1 - reserved for OS kernel
$28 $gp - global pointer
$29 $sp - stack pointer
$30 $fp - frame pointer
$31 $ra - return address

## Slide 11: More Complex Mathematics
Operations must be performed in the appropriate order, storing temporary results
The compiler does this for us.
What if we want to represent the following statement in assembly?
a = b + (c - d) * (e - f) + g

## Slide 12: Example
Convert a = b + (c - d) * (e - f) + g to assembly.
Assume:
b is in $s0
c is in $s1
d is in $s2
e is in $s3
f is in $s4
g is in $s5
We need to break the problem into smaller parts.
x = c - d
y = e - f
z = x * y
h = b + z
a = h + g
Pick unused registers to complete our computation.
let x be $t1
let y be $t2
let z be $t3
let h be $t4
let a be $s6

## Slide 13: Solution
sub $t1, $s1, $s2 #x = c – d
sub $t2, $s3, $s4 #y = e – f
mul $t3, $t1, $t2 #z = x * y
add $t4, $s0, $t3 #h = b + z
add $s6, $t4, $s5 #a = h + g

## Slide 14: Memory Operands
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers (lw)
  Store result from register to memory (sw)
Memory is byte addressed
  Each address identifies an 8-bit byte
Words are aligned in memory
  Address must be a multiple of 4
MIPS is Big Endian
  Most-significant byte at least address of a word
  c.f. Little Endian: least-significant byte at least address

## Slide 15: Memory Operands
g = h + A[8]
  A is an array. Base address of array is $s3.
  G, and h with register $s1, and $s2.
lw $t0, 8($s3) //temporary register $t0 gets A[8]
add $s1, $s2, $t0 // g = h + A[8]

## Slide 16: Memory Operands
100
10
101
1
Data
Memory
0
1
2
3
100
10
101
1
Data
Memory
0
4
8
12
Byte Address
Address

## Slide 17: Memory Operand Example 1
C code:
g = h + A[8];
  g in $s1, h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
    4 bytes per word
lw $t0, 32($s3) # load word add $s1, $s2, $t0
offset
base register

## Slide 18: Memory Operand Example 2
C code:
A[12] = h + A[8];
  h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word

## Slide 19: Registers vs. Memory
Registers are faster to access than memory
Operating on memory data requires loads and stores
  More instructions to be executed
Compiler must use registers for variables as much as possible
  Only spill to memory for less frequently used variables
  Register optimization is important!

## Slide 20: Immediate Operands
Constant data specified in an instruction
addi $s3, $s3, 4
No subtract immediate instruction
  Just use a negative constant
  addi $s2, $s1, -1
Design Principle 3: Make the common case fast
  Small constants are common
  Immediate operand avoids a load instruction

## Slide 21: The Constant Zero
MIPS register 0 ($zero) is the constant 0
  Cannot be overwritten
Useful for common operations
  E.g., move between registers
  add $t2, $s1, $zero

## Slide 22: Exercise
Page 164, problem 2-1
Page 164, problem 2-2

## Slide 23: Unsigned Binary Integers
Given an n-bit number
Range: 0 to +2n – 1
Example
  0000 0000 0000 0000 0000 0000 0000 10112 = 0 + … + 1×23 + 0×22 +1×21 +1×20 = 0 + … + 8 + 0 + 2 + 1 = 1110
Using 32 bits
  0 to +4,294,967,295

## Slide 24: Unsigned Binary Integers
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1
Least significant bit
Most significant bit

## Slide 25: 2s-Complement Signed Integers
Bit 31 is sign bit
  1 for negative numbers
  0 for non-negative numbers
Non-negative numbers have the same unsigned and 2s-complement representation
Some specific numbers
  0: 0000 0000 … 0000
  –1: 1111 1111 … 1111
  Most-negative: 1000 0000 … 0000
  Most-positive: 0111 1111 … 1111

## Slide 26: 2s-Complement Signed Integers
What is the decimal number of this 32 bit two’s complement number?
1111 1111 1111 1111 1111 1111 1111 11002
  = 1× -231 + 1×230 + … + 1×22 +0×21 +0×20 = –2,147,483,648 + 2,147,483,644 = –410

## Slide 27: 2s-Complement Signed Integers
Negate 2ten , and then check the result by negating -2ten
  0000 0000 0000 0000 0000 0000 0000 00102
negating number by inverting the bits and adding 1
  1111 1111 1111 1111 1111 1111 1111 11012 12
1111 1111 1111 1111 1111 1111 1111 11102
+

## Slide 28: Sign Extension
Representing a number using more bits
  Preserve the numeric value
In MIPS instruction set
  addi: extend immediate value
  lb, lh: extend loaded byte/halfword
  beq, bne: extend the displacement
Replicate the sign bit to the left
  c.f. unsigned values: extend with 0s
Examples: 8-bit to 16-bit
  +2: 0000 0010 => 0000 0000 0000 0010
  –2: 1111 1110 => 1111 1111 1111 1110

## Slide 29: Sign Extension
Convert 16-bit binary versions of 810 and -810 to 32-bit binary number

## Slide 30: Activity
On Blackboard…