## Slide 1: Program Counter(PC), Stack, Function, OPcode
Prepared by Dr. Andrew Jung

## Slide 2: Program Counter
Recall that computers use a stored program model
Instructions and data are stored in memory
The next instruction to run is selected and stored in the program counter
This instruction is fetched from memory, decoded, and executed
The Program Counter (PC) is a special register that determines which instruction to run next.
The PC is incremented by 4 after fetching the next instruction to run.
It is not possible to directly modify the value within the PC, but it can be modified indirectly.

## Slide 3: Program Counter
Branches, jumps, and returns indirectly change the value of the PC since they move to a different location in the instruction memory.
From a hardware (HW) perspective, the PC provides the first portion of the fetch, decode, execute cycle.
The PC provides the address of the next instruction to fetch from memory. This instruction is fetched and then decoded by the Control Unit.
The Control Unit signals the executable components of the CPU including the ALU and Registers, and data memory access.

## Slide 4: Assembler memory usage
The "green sheet" at the front of the textbook shows how memory is allocated in the MIPS processor.
Memory is segmented or broken into parts with specific uses
0x0 to 0x00400000 is reserved for use by the Operating System
Note that instructions for input, output, terminating a program, sound, etc., are provided by the operating system, not the CPU.
0x00400000 to 0x10000000 is reserved for instructions - that is, the .text section of your program.
This leaves enough room for 66,060,028 instructions. Many constants may exist here, too.

## Slide 5: Assembler memory usage
0x10000000 to 0x10008000 is the static data section, which is used for data that must exist for the entire runtime of a program such as globals, initialization data for arrays, predefined strings, etc.
0x10008000 onwards - dynamic data segment - grows downward in memory.
  This is also referred to as the heap or free storage.
  Data allocated with new or malloc is stored here.
  This area in memory is used to store dynamically allocated memory.
0xfffffffc up to 0x10008000 - the stack - grows upward in memory toward the free store.
  Data local to each function/subroutine/method is stored here.
  This includes local variables.

## Slide 6: Program Counter
The Program Counter (PC) is a special register that stores the memory location of the next instruction to run.
Instructions are executed in the following manner:
  The address of the next instruction to run is retrieved from the PC
  The instruction is retrieved (fetched) from instruction memory.
  The control unit figures out what to do with the instruction (decode)
    It decides whether to get data from memory or registers.
    It looks at the opcode to see what instruction to run.
    If dealing with a math operation it looks at the function code to see what to tell the ALU to do.
    It tells the program counter whether it should be incremented or a jump should occur.
  The instruction is executed.
  The cycle repeats.

## Slide 7: New Content
The stack contains an Activation Record or Stack Frame for each function.
An activation record or stack frame represents the local variables in a function or method.
The stack is used to keep track of these variables.
For each function/method call, an activation record is created. Each activation record provides a new or fresh set of local variables for a function.

## Slide 8: Stack Pointer
The stack pointer, $sp, provides access to memory in the stack. We may decrement the stack pointer to obtain local memory for a function.
Assembler reads through program and packs into appropriate segments
As it finds labels they are added to a table and later the actual numeric address is filled in.
We'll come back to the stack pointer soon.

## Slide 9: Functions
Functions - a group or module of instructions that performs a specific task
They typically require input (arguments) or produce output (return values).
We want to use functions because they allow us to break up code into manageable parts that are easier to think about (abstract) and they allow us to reuse code.
We don't want functions to do weird things, like modifying data that shouldn't be modified.
Arguments and return values
  Function arguments may be provided with the $a0 to $a3 registers.
  Function return values may be provided using the $v0 and $v1 registers.

## Slide 10: Functions Contd.
You need to find another solution if you need more than 4 arguments or 2 return values.
Think about saved registers and memory.
You should never expect the temporary registers to remain the same after function calls.
You should always expect the saved registers to remain the same, but you might have to return them to their original values.
Making a function call
  Use jal - Jump and Link to call a function and save the return address.
  jal saves the return address so the Program Counter (PC) can be reset to the proper value once you return from the function

## Slide 11: Creating a function
Use a label to name a function. This is done in the same manner as a loop.
label: #The code for your function goes here.
Once you've finished writing your code, be sure to restore any saved registers to their original values.
Be sure to return from the function, too.
To return to the right position in the calling program, call the jr instruction.
jr returns to the address provided in the "return address" register
$ra is the return address register and works to return to the instruction just after the function call.

## Slide 12: Functions
Use jr in the following manner:
jr $ra #return to the calling method or
#function
Let's look at an example of a function
  //A function to add four arguments
  int addFour(int a, int b, int c, int d){
  return a + b + c + d;
  }
  //This function could be called from your main
  //method as follows.
  int x = addFour(1, 2, 3, 4);

## Slide 13: Example in MIPS
#in MIPS the code for your function would be coded as follows
addFour:
  add $v0, $a0, $a1
  add $v0, $v0, $a2
  add $v0, $v0, $a3
  jr $ra
#in the main method you might make your function call and initializations as follows
main:
  li $a0, 1
  li $a1, 2
  li $a2, 3
  li $a3, 4
  jal addFour
  move $s2, $v0 #assume x is stored in $s2

## Slide 14: Opcodes
Review of converting instructions to machine code
In class exercise to review converting instructions from text to binary
Recall that R-type instructions consist of an instruction name and three registers.
For example the following instruction allows us to add the contents of two registers and store the result in another register.
add $t1, $t2, $t3
Remember, all instructions are 32-bit and R-format instructions are divided into multiple components as follows:
  opcode rs rt rd shamt funct
  6-bits 5-bits 5-bits 5-bits 5-bits 6-bits
The opcode and function code for add is represented on the "green sheet" as follows:
opcode / funct
0 / 20 hex

## Slide 15: Opcodes
This means the opcode for add is 0x0 hex and the function code for add is 0x20 hex.
Notice that since the opcode is 0x0 hex, and the opcode is 6 bits, the binary representation of the opcode is 000000.
Recall that each hex value 0, 1, …, 9, A, B, …, E, F may be represented by four bits 0000, 0001, …, 1001, 1010, …, 1110, 1111.
So, the function code for add, should be represented as 0010 0000, but it can only be represented as 10 0000 since there are only six bits available to represent the function code.
So, the representation of add $t1, $t2, $t3 is as follows:
000000 01010 01011 01001 00000 100000

## Slide 16: Opcode Review
Additionally, recall that every four bits of a binary number represent a single hex character 00000001010010110100100000100000
is converted to:
0000 | 0001 | 0100 | 1011 | 0100 | 1000 | 0010 | 0000
which is represented in hex as:
0x014B4820
You can verify the result using MARS. Create a basic MIPS program with your instruction, and press F3 to run the assembler. The hex value for your result should be displayed within the IDE.
Remember, it is important to understand how these conversions are done, so you understand what the assembler is doing for you. It converts assembly instructions to machine code - code that the CPU itself understands.