## Slide 1: Register Format
Prepared by Dr. Andrew Jung

## Slide 2: Representing Instructions
Instructions are encoded in binary
  Called machine code
MIPS instructions
  Encoded as 32-bit instruction words
  Small number of formats encoding operation code (opcode), register numbers, …
Register numbers
  $t0 – $t7 are reg’s 8 – 15
  $t8 – $t9 are reg’s 24 – 25
  $s0 – $s7 are reg’s 16 – 23

## Slide 3: MIPS Instructions
MIPS instructions use 32 bits and come in 3 basic formats.
R format instructions
These are register format instructions. That is, they use only registers.
R-format instructions use the following format:
Opcode rs rt rd shamt func
6 bits 5 bits 5 bits 5 bits 5 bits 6 bits
Recall that instructions are 32-bit.
Notice that 32 = 6+5+5+5+5+6

## Slide 4: MIPS R-format Instructions
Instruction fields
  op: operation code (opcode)
  rs: first source register number
  rt: second source register number
  rd: destination register number
  shamt: shift amount (00000 for now)
  funct: function code (extends opcode)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 5: I format instructions
These are immediate format instructions. These instructions utilize a 16-bit integer value.
I-format instructions use the following format:
Opcode rs rt immediate
6 bits 5 bits 5 bits 16 bits
opcode - instruction type
rt - often the destination register
rs - often the source register
immediate - a 16 bit integer value

## Slide 6: MIPS I-format Instructions
Immediate arithmetic and load/store instructions
  rt: destination or source register number
  Constant: –215 to +215 – 1
  Address: offset added to base address in rs
Design Principle 4: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits

## Slide 7: MIPS Instruction Encoding

## Slide 8: Example
add $s1, $s2, $s5
On the green sheet, the Opcode/Funct is listed. For add it is 0 / 20_hex
0 hex in 6 bits is 000000b - our opcode
20 hex in 6 bits is 100000b - our function code
So our values follow below:
  opcode = 000000b = 0x00
  dest register (rd) = $s1 = $17 --> 0x11 --> 10001
  source register 1 (rs) = $s2 = $18 --> 0x12 --> 10010
  source register 2 (rt) = $s5 = $21 --> 0x15 --> 10101
  function value = 100000

## Slide 9: Example
The binary representation of add $s1, $s2, $s5 is:
000000 10010 10101 10001 00000 100000
opcode rs rt rd shamt func
We can easily convert this to hex by dividing our 32 bit instruction into sections of four bits and finding the hex value for each set of four bits.
0000 0010 0101 0101 1000 1000 0010 0000 --> 0x02558820

## Slide 10: Exercises
With given statement, g = h + A[i].
  What is MIPS assembly code?
  What is the MIPS machine language code for MIPS assembly code?

## Slide 11: Logical Operations
Instructions for bitwise manipulation
Operation | C | Java | MIPS
Shift left | << | << | sll
Shift right | >> | >>> | srl
Bitwise AND | & | & | and, andi
Bitwise OR | ¦ | ¦ | or, ori
Bitwise NOT | ~ | ~ | nor
Useful for extracting and inserting groups of bits in a word

## Slide 12: Shift Operations
shamt: how many positions to shift
Shift left logical
  Shift left and fill with 0 bits
  sll by i bits multiplies by 2i
Shift right logical
  Shift right and fill with 0 bits
  srl by i bits divides by 2i (unsigned only)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 13: Shift Operations
$s0 contains:
  0000 0000 0000 0000 0000 0000 0000 10012 = 910
Shift 4 bits to left
  0000 0000 0000 0000 0000 0000 1001 00002 = 14410
sll $t2, $s0, 4
op and funct  0
rd ($t2)  10
rt ($s0)  16
shamt  4
rs  not used (set to 0)
0 | 0 | 16 | 10 | 4 | 0
OP
rs
rt
rd
shamt
funct
Shift to left by i bits = 2i
Therefore, 24 = 16. The first bit pattern
of this example is 9. Thus, 9 x 16 = 144.

## Slide 14: AND Operations
Useful to mask bits in a word
  Select some bits, clear others to 0
and $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0000 1100 0000 0000
$t0

## Slide 15: OR Operations
Useful to include bits in a word
  Set some bits to 1, leave others unchanged
or $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0011 1101 1100 0000
$t0

## Slide 16: NOT Operations
Useful to invert bits in a word
  Change 0 to 1, and 1 to 0
MIPS has NOR 3-operand instruction
  a NOR b == NOT ( a OR b )
nor $t0, $t1, $zero
0000 0000 0000 0000 0011 1100 0000 0000
$t1
1111 1111 1111 1111 1100 0011 1111 1111
$t0
Register 0: always read as zero